## Slide 1: LSS Green Belt
Practice Questions

## Slide 2
A Green Belt has done a 2-level Full Factorial experiment with 3 factors A, B, and C. The results in the standard order are given in the table here:
What is the effect of factor A? a) 1.5 b) -5 c) 23 d) -10
Notes: C
Step 1 – Split the runs by A’s level
- A = +1 runs:
72, 68, 83, 80
Sum = 303
- A = −1 runs:
60, 54, 52, 45
Sum = 211
Step 2 – Average each group
- Average when A = +1: 303 ÷ 4 = 75.75
- Average when A = −1: 211 ÷ 4 = 52.75
Step 3 – Effect formula
Effect of A = (Average at +1) − (Average at −1)
= 75.75 − 52.75
= 23.0
Result
The effect of factor A is 23.
That means increasing A from low to high boosts the response by an average of 23 units.

## Slide 3
Please have a look at the following ANOVA table.
A p-value is missing. What is the missing p-value?
a) 0.090
b) 0.100
c) 0.192
d) 0.257
Source | SS | DF | MS | F | P
Material | 180 | 3 | 60 | 2.4 | ?
Machine | 225 | 5 | 45 | 1.8 | 0.16
Error | 475 | 19 | 25 |  | 
Total | 880 | 27 |  |  | 
Use F-table
Notes: B
- F‑statistic for Material: 2.4
- Numerator df = 3
- Denominator df = 19
- Minitab gave the cumulative (left‑tail) probability: 0.900290
Right‑tail p‑value:
p = 1 – 0.900290
= 0.099710
That’s about 0.100, which matches option b

## Slide 4
One is designing an experiment with quantitative and qualitative factors.
Which factor is NOT a quantitative factor?
a) Batch
b) Weight
c) Temperature
d) Pressure
Notes: A
- Quantitative factors are measurable on a numeric scale and can take on a range of numerical values. Examples:
- Weight — measured in grams, kilograms, etc.
- Temperature — measured in °C, °F, etc.
- Pressure — measured in pascals, atmospheres, etc.
- Qualitative factors are categorical — they describe qualities or groupings rather than numeric magnitudes.
- Batch is an identifier or category (e.g., Batch 1, Batch 2), not a continuously measurable value. It tells you which group something belongs to, not “how much” or “how many.”

## Slide 5
There is a requirement for a Green Belt to perform a statistical test in order to demonstrate a difference in performance between two processes. The Belt states a Null-Hypothesis and an Alternative Hypothesis, decides to use a confidence level (1- α) = 0.95, calculates the sample sizes needed and conducts the test. The calculated significance of the test statistic is p=0.72.
Which statements describes the result of the statistical test and the conclusion about the processes?
a) The Null-Hypothesis is rejected. The processes are different.
b) The Null-Hypothesis is not rejected. There is not enough evidence that the processes are different.
c) The Alternative-Hypothesis is rejected. The processes are different.
d) The Alternative-Hypothesis is accepted. The processes are different
Notes: B
The p‑value here is 0.72, which is much larger than the chosen significance level α = 0.05.
Step‑by‑step reasoning
Decision rule:
  If p ≤ α → Reject H_0 (Null Hypothesis)
  If p > α → Fail to reject H_0
Apply the rule:
  0.72 > 0.05 → Fail to reject H_0
Interpretation:
There’s no statistical evidence strong enough to claim a difference between the two processes.
This doesn’t “prove” the processes are identical; it means the data didn’t reveal a significant difference at the 95 % confidence level.

## Slide 6
If production cannot meet demand, it is usually most effective to reduce:
a) Takt time
b) Lead time
c) Set-up time
d) Cycle time
Notes: D
Cycle time is the actual time it takes to produce one unit during steady-state operation. - Throughput (units/hour) is the inverse of cycle time. Lowering cycle time directly raises how many units you can make in the same period. - Unlike setup time (which only affects runs that change over) or lead time (which includes non-production steps), cycle time impacts every single unit produced.
Takt time: Planning metric for matching demand, not a process parameter you can cut
Lead time: Total order-to-delivery time; shortening it may improve customer service but doesn’t boost production rate
Set-up time: Valuable to reduce, but only affects batches requiring changeover
Cycle time: Directly governs production rate for every unit; reducing it scales throughput immediately

## Slide 7
What is a "time series plot" also called?
a) Deming chart
b) Pareto chart
c) Gantt chart
d) Run chart
Notes: D
A time series plot displays data points in time order and is commonly called a run chart. It shows how a measure changes over time on the horizontal axis.
A Deming chart is another name for a control chart that adds control limits to a run chart.
A Pareto chart ranks categorical data by frequency or impact.
A Gantt chart visualizes project schedules, not process data over time.

## Slide 8
What is the definition of Rolled Throughput Yield (RTY)?
a) Yield from the last step of a process that has a series of further steps to complete
b) Probability that a unit will pass every step within a process with zero defects
c) Number of defects from a single process step divided by the number of produced units
d) Total number of good units of all consecutive process steps divided by the number of produced units
Notes: B
Rolled Throughput Yield (RTY) is a Six Sigma metric that measures the likelihood that a single unit can pass through an entire process from start to finish without needing rework or producing defects.
Key points:
- Calculated by: Multiplying the first-pass yields of each process step together.
- Focus: Process capability and quality across all steps, not just the last one.
Why it matters:
- Shows the true cost of poor quality
- Highlights cumulative effects of defects over multiple steps
- Encourages fixing issues at the sourc

## Slide 9
It is possible to look at any organization on the three main levels: primary process, department and
management.
Which level would have both Key Process Input Variables (KPIV) and Key Process Output Variables (KPOV)?
a) Primary process only
b) Primary process and department only
c) Primary process and Management only
d) All three of them
Notes: D
All three organizational levels — primary process, department, and management — have both Key Process Input Variables (KPIVs) and Key Process Output Variables (KPOVs).
At each level, inputs (KPIVs) influence the process, and outputs (KPOVs) measure its results:
Primary process: material quality, equipment settings → yield, defects
Department: staff skills, workflow → productivity, delivery rate
Management: strategic choices, budgets → profitability, customer satisfaction This reinforces that improvement opportunities and measurable results exist at every level of the organization.

## Slide 10
A doctor hypothesises that there is a correlation between the heights of sons and their fathers. He
records the heights of 12 fathers and sons in cm. The results are shown in the table:
Use significance level α= 0.05.
How should the correlation between the heights of fathers and sons be evaluated?
a) Pearson correlation of father and son = 0.691, p-value = 0.013. The correlation is NOT significant.
b) Pearson correlation of father and son = 0.309, p-value = 0.073. The correlation is significant.
c) Pearson correlation of father and son = 0.691, p-value = 0.013. The correlation is significant.
d) Pearson correlation of father and son = 0.309, p-value = 0.073. The correlation is NOT significant.
Father | 165 | 160 | 170 | 163 | 173 | 157 | 178 | 168 | 173 | 170 | 175 | 180
Son | 173 | 168 | 173 | 165 | 175 | 168 | 173 | 165 | 180 | 170 | 173 | 178
Notes: C
Step‑by‑Step in Minitab
Enter the Data
  In C1, type the fathers’ heights: 165 160 170 163 173 157 178 168 173 170 175 180
  In C2, type the sons’ heights: 173 168 173 165 175 168 173 165 180 170 173 178
Run the Correlation
  Go to Stat > Basic Statistics > Correlation.
  In the Variables box, select both columns (C1 and C2).
  Click OK.
Read the Output
  Minitab will display the Pearson correlation coefficient (r) and the p-value.
  Compare the p‑value to α = 0.05:
  p < 0.05 → Significant correlation.
  p ≥ 0.05 → Not significant.
Interpret
Here, r = 0.691 and p = 0.013, so:
Positive correlation: as father’s height increases, son’s height tends to increase.

## Slide 11
Who is the right person to remove barriers arising in a Lean Six Sigma improvement project?
a) The Process Owner (customer of the improvement project)
b) The Project Leader
c) The Master Black Belt
d) The Champion
Notes: D
Key points:
- Senior leader who sponsors the project
- Has authority to remove organizational roadblocks
- Ensures project aligns with strategic goals
- Supports team when issues exceed Project Leader’s control
Why not others?
- Process Owner: Owns process, doesn’t typically remove major obstacles
- Project Leader: Manages execution, escalates but lacks top authority
- Master Black Belt: Provides technical/method guidance, not organizational power

## Slide 12
What is the most important factor in the successful implementation of Lean Six Sigma?
a) The necessary resources available
b) The top management supporting and leading the implementation
c) Clear customer requirements
d) An extensive training program
Notes: B
Top management supporting & leading the implementation
Key Points:
- Sets vision, urgency, and alignment with strategy
- Controls resources (budget, staff, cross‑team cooperation)
- Drives cultural adoption by modeling Lean Six Sigma principles
- Overcomes resistance and keeps priorities on track
Why not others?
- Necessary resources: Important, but leadership secures & directs them
- Clear customer requirements: Essential, but meaningless without leader commitment
- Extensive training: Builds skills, but impact is limited without top‑level mandate

## Slide 13
Which control chart is normally used when monitoring the number of defects per shipment?
a) P chart
b) U chart
c) NP chart
d) C chart
Notes: B
Key Points:
- Used to track defects per unit when sample sizes vary
- Handles variable shipment sizes effectively
- Monitors defect density (e.g., defects per shipment, per batch, per item)
- Suitable when multiple defects can occur in a single unit
Why not others?
- P Chart: Tracks proportion of defective units, not defects per unit
- NP Chart: Counts defective units with constant sample size
- C Chart: Counts total defects, assumes constant sample size

## Slide 14
What is the importance of the 'reaction plan' in a control plan?
a) It lists how often the process should be monitored
b) It indicates that a new team must be formed to solve a problem
c) It defines the special characteristics to be monitored
d) It describes what should happen if a key variable goes out-of-control
Notes: D
Key Points
- Specifies immediate corrective actions to take when monitoring shows an out‑of‑control condition
- Ensures quick, consistent response to prevent defects or non‑conformance
- Minimizes downtime and impact on quality
- Part of proactive process control to maintain stability
Why not others?
- Lists monitoring frequency: That’s part of the measurement section, not the reaction plan
- Indicates new team formation: Not the function of a reaction plan
- Defines special characteristics: Belongs in the characteristics/specification sectio

## Slide 15
Which tool is suitable to compare data measured in categories?
a) Pareto Chart
b) Cause and Effect diagram
c) Bar Chart
d) Histogram
Notes: C
Key Points:
- Displays data for different categories side by side
- Easy comparison of sizes, counts, or frequencies across categories
- Works for qualitative (categorical) data
- Bars can be vertical or horizontal for readability
Why not others?
- Pareto Chart: Special type of bar chart arranged in descending order, focuses on prioritization (80/20 rule)
- Cause & Effect Diagram: Identifies possible causes, not used for numerical comparison
- Histogram: Shows frequency distribution of continuous data, not distinct categories

## Slide 16
What does an asterix in a boxplot mean?
a) Target data point
b) Removed data point
c) Optimum data point
d) An outlier data point
Notes: D
Key Points:
- In boxplots, asterisks (or sometimes dots) mark outliers
- Outliers = values significantly higher or lower than most of the dataset
- Typically lie beyond 1.5 × IQR (Interquartile Range) from the box edges
- Highlight unusual data that may need investigation
Why not others?
- Target data point: Boxplots don’t indicate targets with symbols
- Removed data point: Asterisks represent included but extreme values, not removed ones
- Optimum data point: Boxplots don’t identify optimum values

## Slide 17
Please see the table below.
What is the temperature main effect in this 2k factorial experiment?
a) -15
b) -1
c) 13
d) 15
Notes: C
- Main effect = difference in average yields at high vs. low temperature
- Low Temp Avg: (62 + 56) ÷ 2 = 59
- High Temp Avg: (74 + 70) ÷ 2 = 72
- Effect: 72 − 59 = 13
- Positive value → higher temperature increases yield by 13 units on average

## Slide 18
Please read the list below.
1. Project Board members
2. Process Owners
3. Master Black Belts
4. Black Belts
Which person can most likely fill the function of a coach in Six Sigma organizations?
a) 1 and 2 only
b) 2 and 3 only
c) 3 and 4 only
d) All of the persons mentioned
Notes: C
Key Points:
- Master Black Belts (MBBs):
- Act as primary coaches/mentors to Black Belts and Green Belts
- Provide expert guidance on tools, methodology, and project selection
- Ensure alignment with Six Sigma standards across the organization
- Black Belts (BBs):
- Coach Green Belts and project teams within their functional areas
- Offer practical, hands‑on advice during project execution
Why not others?
- Project Board members: Provide strategic oversight, not day‑to‑day coaching
- Process Owners: Manage processes and sustain improvements, not typically focused on coaching roles

## Slide 19
What information does a box plot provide?
a) The average of our sample
b) Sample size
c) The median and the quartiles of our sample
d) Standard deviation of our sample
Notes: C
Key Points:
- Displays median (middle value) of the dataset
- Shows lower (Q1) and upper (Q3) quartiles → middle 50% of data
- Visualizes minimum and maximum values (excluding outliers)
- Highlights outliers separately with symbols like dots or asterisks
- Gives a quick view of data spread and symmetry
Why not others?
- Average: Not directly shown in a box plot
- Sample size: Not indicated unless annotated separately
- Standard deviation: Not part of box plot display

## Slide 20
A belt is designing a hypothesis test to detect a specified difference between two processes. The
significance level α of the test is 5% and the power (1-β) = 70%. Later, he decides to increase the
power of the test to 90%. He does not change the significance level.
What will be the effect of this change?
a) The process variability will improve
b) The sample size of the test will increase
c) The probability of rejecting the null hypothesis will decrease
d) The probability of rejecting the null hypothesis will increase
Notes: B
Test power (1−β) = probability of detecting a true difference.
Increasing power from 70% → 90% makes the test more sensitive.
With α unchanged, achieving higher power requires a larger sample size to reduce variability and improve detection.
This reduces Type II errors but does not change α.

## Slide 21
Obstacles to the effectiveness of equipment can be categorized in ‘Availability’, ‘Performance’
and ‘Quality’.
Which failure is a 'Performance' loss?
a) Setup and adjusting before good product is made
b) Process losses due to rework
c) Minor stoppages due to problems with material flow
d) Equipment failure from breakdowns
Notes: C
Key Points:
- Performance losses occur when equipment runs slower than its designed speed or experiences frequent, brief interruptions
- Minor stoppages (e.g., jams, misfeeds, brief halts for adjustments) reduce throughput without being counted as downtime
- They differ from:
- Availability losses: e.g., setups, adjustments, breakdowns
- Quality losses: e.g., defects, rework
Why not others?
- Setup & adjusting: Availability loss
- Rework losses: Quality loss
- Equipment breakdowns: Availability loss

## Slide 22
A team leader has been asked to do a capability and performance analysis on a process.
Although the data collected from each rational subgroup is normally distributed, the data from the
process as a whole is clearly not distributed normally.
1. Capability analysis for each sub-group based on normal distribution assumption
2. Use a Box-Cox or Johnson transformation and then analyze the process data with the standard tool
3. Identify the distribution and use a method that is based on the non-normal distribution
4. Perform a Z-transformation then analyze the process data with the standard tool
Which tools might be used in this analysis?
a) 1, 2, 3
b) 1, 2, 4
c) 1, 3, 4
d) 2, 3, 4
Notes: A
Capability by subgroup (normal): Appropriate because each rational subgroup is normal; analyze capability within each subgroup using standard normal-based tools.
2. Box-Cox/Johnson transformation: Appropriate to stabilize variance/normalize whole-process data, then apply standard capability analysis.
3. Fit a non-normal distribution: Appropriate to model the actual process distribution (e.g., Weibull, lognormal) and use non-normal capability methods.
4. Z-transformation: Not appropriate; standardizing to z-scores rescales but does not make non-normal data normal.

## Slide 23
A production process is reported to have a Cp of 2.0 and a Cpk of 1.5. The process has a spread
(6 sigma) of 12 units.
What is the tolerance interval?
a) 6 units
b) 12 units
c) 18 units
d) 24 units
Notes: D
Given:
- Cp = 2.0
- Process spread (6σ) = 12 units
- Formula: Cp = (Tolerance) ÷ (Process spread)
Calculation:
Tolerance (USL – LSL) = Cp x Process spread = 2.0 x 12 = 24 units
Key Insight:
- Cp compares specification width (tolerance) to process width (6σ)
- Higher Cp ⇒ Wider tolerance relative to process spread ⇒ Greater potential capability

## Slide 24
What do Lean and Six Sigma NOT share?
a) A focus on customer satisfaction
b) A required commitment from top management
c) A focus on continuous improvement
d) A required long learning curve
Notes: D
Shared focus areas:
Customer satisfaction
Top management commitment
Continuous improvement
Key difference:
Lean: Generally faster to learn and implement; tools are intuitive and visual
Six Sigma: Requires more in‑depth statistical training, but not inherently a “long” learning curve
Neither methodology requires a long learning curve — it depends on application scope and depth

## Slide 25
After returning from a two-week vacation a manager reviewed the Xbar and R charts that were
maintained during the manager’s absence. One of the Xbar charts shows the last 50 points to be
very near the centre line. In fact, they all seem to be within about one sigma of the centre line.
What is the BEST explanation for this occurrence?
a) Somebody restored the wider control limits according to the original calculation
b) The process standard deviation has decreased and the control limits were not recomputed
c) There has been poor quality performance for quite some time
d) It shows that the operators did a very good job keeping the process close to target
Notes: B
- Observed pattern: 50 consecutive points within ~1σ of the centre line
- Best explanation: Process variation (σ) decreased → data tightly clustered
- Impact: Control limits based on old, larger σ are now too wide → gives false impression of extreme stability
- Lesson: Always recalculate control limits when process variation changes

## Slide 26
A graphical tool used to rank the occurrence of defects from very frequently to less frequently is:
a) Pareto Chart
b) Scatter Diagram
c) Check Sheet
d) Bar Chart
Notes: A
Purpose: Highlights the most significant defect types by ordering them from most frequent to least frequent Principle: Based on the 80/20 rule — a small number of causes often account for the majority of problems
Usage: Helps prioritize improvement efforts by focusing on the “vital few” issues rather than the “trivial many”
Visual form: Bars arranged in descending order, often with a cumulative percentage line

## Slide 27
Plese read the following list:
1. Poka-yoke
2. 5S
3. TPM
4. Kanban
Which techniques support operational control?
a) 1, 2, 3 and 4
b) 1, 2 and 4
c) 2 and 4 only
d) 2, 3, and 4
Notes: A
- Poka‑yoke: Error‑proofing devices/methods to prevent defects at source
- 5S: Workplace organization for consistent, efficient operations
- TPM (Total Productive Maintenance): Engages all levels to maintain equipment at optimal condition
- Kanban: Visual workflow control to manage production and inventory efficiently
- All four contribute directly to operational control by standardizing processes, reducing waste, and ensuring smooth flow

## Slide 28
See the dataset below:
7, 6, 9, 8, 5, 7
What is the standard deviation?
a) 1.2
b) 1.4
c) 1.9
d) 2.0
Notes: B
Standard Deviation Calculation
Dataset: 7, 6, 9, 8, 5, 7
Step 1 – Mean:
(7+6+9+8+5+7)/6 = 42/6 = 7
Step 2 – Deviations from Mean & Squared Deviations:
- (7 − 7)² = 0
- (6 − 7)² = 1
- (9 − 7)² = 4
- (8 − 7)² = 1
- (5 − 7)² = 4
- (7 − 7)² = 0
Step 3 – Variance:
- Sum of squares = 0 + 1 + 4 + 1 + 4 + 0 = 10
- Sample variance = 10/(n-1) = 10/5 = 2
Step 4 – Standard Deviation:
s = square root of 2 = 1.41
Open Minitab and ensure you’re on a blank worksheet. Enter the data in one column:
  Click on cell C1, type Data, press Enter.
  Enter: 7, 6, 9, 8, 5, 7 (each in a separate row under Data).
Go to: Stat → Basic Statistics → Display Descriptive Statistics.
In the Variables box, select your column Data.
Click OK to run the command.
Output window will show StDev ≈ 1.4142 (round to 1.4).

## Slide 29
In the table below, seven numbered parts are weighed on two scales. Test the null-hypothesis that
scale A and B give equal results.
Which statement is true?
a) There is a significant difference between both scales, with p=0.017
b) There is no significant difference between both scales, with p=0.930
c) There is a significant difference between both scales, with p=0.047
d) There is no significant difference between both scales, with p=0.825
Notes: A
Paired t‑test in Minitab
1. Enter your data
Open Minitab.
In C1, type Scale A and enter the values: 255, 206, 250, 212, 252, 220, 182
In C2, type Scale B and enter the values: 257, 213, 257, 215, 256, 221, 182
2. Open the paired t‑test tool
Go to the Stat menu → Basic Statistics → Paired t.
3. Set up the analysis
In the Paired t dialog box:
  For First sample, select Scale A
  For Second sample, select Scale B
Make sure the option Paired is selected (it should be, by default).
4. Configure options (optional)
Click Options… if you want to:
  Set the confidence level (default is 95%).
  Choose a two‑tailed test (default).
5. Run the test
Click OK to run it.
6. Interpret the results
Minitab will output:
  Mean difference
  Standard deviation of differences
  t‑value, degrees of freedom
  p‑value
In this case, you’ll see p ≈ 0.017, which means:
  Significant difference at the 5% level

## Slide 30
When planning an experiment, a series of steps must be followed. To make a successful
experiment possible, which step is the most important?
a) Provide enough time and resources to run the experiment
b) Provide clear instructions to the operators performing the experiment
c) Make a test plan, including the objectives of the experiment
d) Prepare all samples needed for the experiment
Notes: C
The backbone of any successful experiment is good planning — without it, the other steps can fall apart.
While time, resources, clear instructions, and prepared samples are all essential, the most important foundation is:
Make a test plan, including the objectives of the experiment
Why this is key:
Sets the direction – Everyone involved knows the purpose and what’s being measured.
Identifies variables – You can control sources of variation before they creep in.
Aligns resources – Time, people, and materials can be organised around a clear goal.
Avoids waste – Prevents running an experiment that doesn’t actually answer your question.
A clear test plan acts like a roadmap — it ensures the other steps (time/resources, instructions, samples) are efficient and effective, rather than scattered efforts.

## Slide 31
Who is considered to be the stakeholder in a Lean Six Sigma process?
a) The Director
b) The Sales Department
c) The Production Manager
d) All who have an interest in the outcome of the project
Notes: D
In Lean Six Sigma, stakeholders are defined broadly — they’re not just leaders or a single department, but anyone impacted by, contributing to, or invested in the outcome of the project.
Why this matters in Lean Six Sigma:
Holistic perspective – Processes touch multiple parts of an organisation, so you need input from all affected groups.
Buy‑in & support – Engaging all stakeholders increases cooperation and smooths implementation.
Sustainable results – Solutions are more likely to stick if the people affected are involved in shaping them.
Stakeholders can include frontline operators, managers, customers, suppliers, quality teams — essentially anyone with a vested interest in the process or its results.

## Slide 32
Which statements is the best definition of 'Takt Time’?
a) The maximum operating speed of a process or production line
b) The long-run historic performance capacity of a system
c) Pace of a manufacturing system as determined by customer demand
d) Average time taken to complete a task under normal operating conditions
Notes: C
Takt Time = Pace of a manufacturing system as determined by customer demand.
- From German Takt = “pulse/beat” of production.
- Formula: Takt Time = Available production time ÷ Customer demand.
- Aligns output with demand to avoid overproduction or delays.

## Slide 33
What test is used for testing significance in an analysis of variance (ANOVA) table?
a) T test
b) Z test
c) F test
d) Chi square test
Notes: C
ANOVA Significance Test
- ANOVA uses the F‑test to determine if there are significant differences between group means.
- Why F‑test? It compares the ratio of variance between groups to variance within groups.
- Large F values → higher likelihood that at least one group mean is different

## Slide 34
What determines Takt Time?
a) Warehousing
b) Customer demand
c) Planning
d) Production
Notes: B
Takt Time is determined by: Customer demand
- From German Takt = “pulse/beat” of production.
- Formula: Takt Time = Available production time ÷ Customer demand.
- Ensures production pace matches what customers actually require.

## Slide 35
As a Lean professional, you are asked to implement a Lean tool to improve the visibility of
problems in a process.
Which tool is the best choice to start with?
a) Jidoka
b) 5S
c) Kanban
d) 5 Whys
Notes: B
Why:
- Organises the workplace so abnormalities stand out immediately.
- Steps: Sort, Set in order, Shine, Standardise, Sustain.
- A clean, well‑ordered environment makes issues (e.g., misplaced tools, leaks, defects) visible at a glance.
- Acts as a foundation for other Lean tools by creating transparency in the process.

## Slide 36
A producer of television programs receives complaints about the length of programs made. Too
often the length of a program does not fit within the upper and lower limits specified of its
customer. Within an improvement project, a Black Belt carries out a measurement system
analysis.
Which measure is chosen to assess the reliability of the data?
a) % Study Variation (% R&R)
b) % Contribution
c) % Tolerances (% P/T)
d) Number of Distinct Categories
Notes: C
MSA metric to assess data reliability (with spec limits)
Why: Compares measurement variation to customer tolerance; ideal when U/L spec limits drive accept/reject.
→ lower is better (≈ ≤10% good, 10–30% marginal, >30% poor).
Not the others:
% Study Variation (%R&R): vs. process variation, not specs.
% Contribution: variance breakdown, not an acceptability metric.
NDC: discrimination/resolution, not reliability vs. specs.

## Slide 37
Two young English men, Harry and Edward, love target shooting with rifles. In a contest between
them, a Black Belt measured the distance of the shots to the target in cm. He used 15 of Harry's
shots and 25 of Edward's shots and calculated the standard deviations. The standard deviation of
Harry is 3.2 and of Edward 2.8.
When using alpha equal to 5%, what is the outcome of testing the null hypothesis that the
variances of both are equal?
a) F-Statistic is 1.14 and p-value is 0.749. Variances are equal.
b) F-Statistic is 1.14 and p-value is 0.027. Variances are NOT equal.
c) F-Statistic is 1.31 and p-value is 0.547. Variances are equal.
d) F-Statistic is 1.31 and p-value is 0.034. Variances are NOT equal.
Notes: C
Steps in Minitab
Open the test
  Go to Stat → Basic Statistics → 2 Variances.
Select the data type
  In the dialog box, choose Summarized data.
Enter each group's stats
  For Sample 1 (Harry):
    Sample size (n_1) = 15
    Standard deviation (s_1) = 3.2
  For Sample 2 (Edward):
    Sample size (n_2) = 25
    Standard deviation (s_2) = 2.8
Set your options
  Click Options, set confidence level to 95% (α = 0.05).
  Hypothesized ratio = 1 (H₀: variances are equal).
Run and read output
  Minitab will calculate: [ F = \frac{s_12}{s_22} = \frac{3.22}{2.82} \approx 1.31 ]
    F-Statistic ≈ 1.31
    p-value ≈ 0.547
  Since p-value > 0.05 → fail to reject H₀ → variances are equal.

## Slide 38
Value Stream Mapping (VSM), current state, is a method that fits into one of the DMAIC phases.
What is this phase called?
a) Improve
b) Control
c) Measure
d) Analyse
Notes: D
Check the manual (6.4 value Stream Analysis)

## Slide 39
Please read the list below:
1. Normal
2. Poisson
3. Binomial
4. Chi-Square
Which are discrete probability distributions?
a) 1 and 2 only
b) 1 and 4 only
c) 2 and 3 only
d) 3 and 4 only
Notes: C
1. Normal → Continuous (bell‑shaped curve over a continuous range)
2. Poisson → Discrete (counts of events in a fixed interval)
3. Binomial → Discrete (counts of successes in fixed number of trials)
4. Chi‑Square → Continuous (distribution of a sum of squared variables, often used in tests of variance or independence)

## Slide 40
An effective quality system is characterised by formal documents. What document describes how
to accomplish specific tasks?
a) Machine Instruction Manual
b) Work instructions
c) The quality manual
d) Records and forms
Notes: B
Provide step‑by‑step guidance for performing a task correctly and consistently.
Ensure operators, technicians, or staff follow the same method, reducing variation.
Are more detailed than procedures, often including diagrams, photos, or checklists.

## Slide 41
How is hypothesis testing used to make a statement about a population?
a) Taking a random sample size of 5
b) Taking a selective sample of 5
c) Taking a sample of which the size is not important
d) Taking a large enough random sample
Notes: D
Hypothesis testing uses sample data to make inferences about an entire population.
For results to be statistically valid:
  The sample must be random (every member has an equal chance of being selected, reducing bias).
  The sample must be large enough to accurately estimate population parameters and detect meaningful effects.
This approach allows us to calculate probabilities (p‑values) that help decide whether to reject or fail to reject the null hypothesis.

## Slide 42
One is asked to identify all factors that could possibly contribute to a process problem.
Which problem-solving tool would be the best choice to use in this situation?
a) Cause and Effect matrix
b) Fishbone diagram
c) Pareto diagram
d) Histogram
Notes: B
Why it’s best here:
Purpose: It’s designed to brainstorm and visually map all possible causes of a problem, grouped into logical categories (e.g., Methods, Machines, Materials, People, Environment, Measurement).
Benefit: Encourages a comprehensive exploration rather than jumping to conclusions, which is crucial when you want to uncover every potential factor.
Structure: The diagram’s “spine” represents the problem, while the “bones” branch out into categories of potential causes.
Why not the others:
Cause and Effect matrix: Ranks and prioritizes causes already identified, not for broad initial brainstorming.
Pareto diagram: Highlights the most significant causes based on data, but only after you’ve identified them.
Histogram: Shows data distribution or variation, not causal relationships.

## Slide 43
A Six Sigma Black Belt has designed a 2-level full factorial experiment. The total number of experimental runs is 128. There are no replicates.
How many factors are varied in the experiment?
a) 5
b) 6
c) 7
d) 8
Use this in exam
Notes: C

## Slide 44
Which is an example of continuous data?
a) Height of adult men
b) Result of a throw of a dice
c) Number of defective products
d) Bolt fits yes or no in the nut
Notes: A
Continuous data can take on any value within a given range, including fractional or decimal measurements.
Height is measured on a continuous scale — someone could be 170 cm, 170.2 cm, 170.25 cm, etc.
Other examples: weight, temperature, time.
Why not the others:
b) Result of a throw of a dice → Discrete; only specific whole-number outcomes (1–6).
c) Number of defective products → Discrete; counts (0, 1, 2…) without fractional parts.
d) Bolt fits yes or no in the nut → Categorical/Binary; just two possible categories (yes/no).

## Slide 45
Which statement about the p-value is true?
The (1-p) -value is the probability that the alternative hypothesis is true
The p-value is the probability of obtaining a test statistic at least as extreme as the one that was actually observed, assuming that the null hypothesis is true
The p-value is the probability of falsely rejecting the null hypothesis
The p-value is the probability that the null hypothesis is true
Notes: B
Definition: The p‑value answers the question: "If the null hypothesis were true, how likely is it that we'd see data this extreme (or more extreme) just by random chance?"
It’s a conditional probability: [ p = P(\text{data as extreme as observed} \mid H_0 \ \text{is true}) ]
A small p‑value suggests the observed data would be unusual under ( H_0 ), which can lead you to reject the null hypothesis.
❌ Why the others are wrong
(1 − p) is the probability the alternative hypothesis is true → Incorrect; p‑values don’t directly give the probability of ( H_a ) or ( H_0 ) being true.
The p‑value is the probability of falsely rejecting ( H_0 ) → That’s the Type I error rate (( \alpha )), not the p‑value.
The p‑value is the probability that ( H_0 ) is true → Not correct; we can’t assign this probability without a Bayesian framework and prior beliefs.

## Slide 46
Please see the following characteristics:
1. Preventing mistakes
2. Preventing overproduction
3. Parts are delivered at the right time
4. Parts are delivered in the correct quantity
Which characteristics belong to Pull?
a) 1, 2, 3
b) 1, 2, 4
c) 1, 3, 4
d) 2, 3, 4
Notes: D
Why these belong to Pull
In Lean manufacturing, the Pull system means work is triggered only by actual demand — nothing is made or moved unless the next step or customer needs it.
2) Preventing overproduction → Core benefit of Pull; produces only what’s needed, when it’s needed.
3) Parts are delivered at the right time → Just‑In‑Time delivery is a hallmark of Pull, reducing inventory waste.
4) Parts are delivered in the correct quantity → Matches supply to actual demand, avoiding surplus.
Why “Preventing mistakes” (1) isn’t part of Pull
That’s linked to Poka‑Yoke (error‑proofing), which focuses on quality assurance, not on demand‑driven flow.

## Slide 47
Which term used to describe the risk of a Type II error in a hypotheses test?
a) Confidence level
b) Power
c) Alpha risk
d) Beta risk
Notes: D
Type II error = Failing to reject the null hypothesis when it is actually false (a “miss”). The probability of making a Type II error is denoted by β (beta).
This is often called beta risk.
Power of a test = 1 - \beta, which is the probability of correctly rejecting a false null hypothesis.
Why not the others:
a) Confidence level → Linked to 1 - \alpha in confidence intervals, not Type II errors.
b) Power → Related, but it’s the complement of beta risk.
c) Alpha risk → Probability of a Type I error (rejecting a true null hypothesis).

## Slide 48
Which defects per million opportunity (DPMO) level approaches five sigma quality?
a) 3.4
b) 32
c) 233
d) 1350
Notes: C
In Six Sigma terms (using the standard 1.5 σ long‑term shift), five‑sigma quality delivers about 99.977% yield — which works out to roughly 233 defects per million opportunities.

## Slide 49
A Six Sigma Belt has designed an experiment with 5 factors, and wants to examine the interaction
between two factors: Speed and Temperature. 4 levels have been selected for Speed and 3 levels
for Temperature.
How many degrees of freedom does this interaction have?
a) 2
b) 4
c) 6
d) 12
Notes: C
Speed = 4 levels → 4 - 1 = 3 DOF
Temperature = 3 levels → 3 - 1 = 2 DOF
Interaction DOF = = 6 (2 x 3)

## Slide 50
Which chart is used to monitor the number of defective parts in a sample?
a) C Chart
b) NP Chart
c) Xbar-R Chart
d) I-MR Chart
Notes: B
Key Points:
NP Chart → Tracks the number of defective units (pass/fail) in a constant‑size sample.
Data type: Attribute (count data, not measurements).
Use when: You care about “how many items failed” rather than “how bad” the defect was.
Other charts for context:
C Chart → # of defects per unit (can be multiple per unit).
X̄‑R Chart → Mean and range of continuous measurements.
I‑MR Chart → Individual values and moving range.

## Slide 51
Which is NOT an example of Visual Management?
a) Operating instructions
b) Process flow mapping
c) Visual inspection
d) Publication boards with pictures
Notes: C
Visual inspection, while it sounds “visual,” is actually a method of detecting defects, not a visual signal to manage the process.

## Slide 52
The process map known as SIPOC provides team members an understanding of the process.
From which level is this view of process taken?
a) A very high level
b) A very detailed level
c) Floor level
d) The customer's perspective
Notes: A
SIPOC = Suppliers, Inputs, Process, Outputs, Customers
Used early in process improvement to give an overview of the entire process.
Shows the start‑to‑finish flow without going into detailed steps.
Key Point:
It’s a high‑level map — zoomed‑out enough to see all major elements and relationships.
Helpful for aligning the team’s understanding before diving into detailed analysis.
Think of it like looking at a roadmap of an entire country before zooming into street‑level directions.

## Slide 53
The objective of Value stream mapping is:
a) To map all non-value adding activities
b) To map all necessary activities
c) To map value adding activities
d) To identify all the above-mentioned activities
Notes: D
Value Stream Mapping (VSM) = A Lean tool to visualize the entire process flow, from start to finish, showing value‑adding, non‑value‑adding, and necessary activities.
Purpose:
Spot where value is created.
Highlight waste (non‑value‑adding).
Show essential but non‑value‑adding steps (support activities).
Enable targeted improvement.
Key takeaway: VSM isn’t just about good steps — it’s about seeing everything, so you know where to cut waste and where to improve flow.

## Slide 54
An X-bar & Range control chart is based on a sample size of 4. An employee mistakenly samples
2 parts instead of 4. He plots the average and the range of the two observations on the control
chart.
Which conclusion should be drawn?
a) It increases the probability that the Xbar chart shows an out-of-control condition
b) It will not cause any misjudgements if the process is in control
c) The points will always be plotted near the centerlines of the charts
d) It increases the probability that the R chart shows an out-of-control condition
Notes: A
Control limits for an X̄‑R chart are based on the intended sample size (here, n = 4). If you take n = 2 instead, the natural variability of the subgroup average increases.
That means plotted points are more likely to fall outside the control limits on the X̄ chart — even if the process hasn’t truly changed.
The R chart limits also change with subgroup size, but here the biggest impact is on the X̄ chart misjudgement risk.
Key takeaway: Always use the sample size your control chart was designed for — wrong n = misleading signals.

## Slide 55
What does Takt Time mean?
a) The shortest time between consecutive customer orders
b) The average time between order and delivery
c) The average time between consecutive customer orders
d) The average time between consecutive order deliveries
Notes: C
Takt Time = The pace at which products must be produced to meet customer demand.
Takt Time = Available production time/Customer demand
Key Points:
Represents the average time between the start of production of one unit and the start of the next, based on demand.
Aligns production speed to customer pull, preventing overproduction.
Comes from the German word Takt, meaning “pulse” or “beat,” like the rhythm in music.
Think of it as the heartbeat of your production line — beat too slow, customers wait; beat too fast, you overproduce.

## Slide 56
Which statement concerning WIP is the most true for a pull production system?
a) No WIP
b) Constant WIP
c) High WIP
d) Low WIP
Notes: B
Pull production system (e.g., Kanban) = Work is authorized only when there’s downstream demand.
WIP (Work in Process) behaviour:
WIP levels are limited and kept constant using visual controls (e.g., Kanban cards).
Prevents overproduction and smooths workflow.
Any bottleneck or problem becomes visible quickly.
Why not the others:
No WIP → Unrealistic; some WIP is needed to keep flow going.
High WIP → Typical of push systems, causes delays and waste.
Low WIP → Desirable but in pull systems it’s controlled and consistent, not randomly low.
Key takeaway: In a pull system, WIP is like a fixed‑size container — it doesn’t expand or shrink unless the system design changes.

## Slide 57
In which phase of a project is a Project Charter created?
a) Project evaluation
b) Project planning
c) Project initiation
d) Project execution
Notes: C
Project Charter = The formal document that authorizes a project and gives the project manager authority to use organizational resources.
Created in:
Project Initiation phase — the very start of the project life cycle.
Sets out the project’s objectives, scope, stakeholders, high‑level schedule, and budget.
Purpose:
Provides clarity and alignment before detailed planning begins.
Acts as the agreement between sponsor and project team on what’s being delivered.
Key takeaway: The charter is your project’s birth certificate — it officially brings the project into existence.

## Slide 58
Which of these tools can form part of "Visual Management"?
a) WIP board
b) Kanban signals
c) Process maps
d) All of the above
Notes: D
Visual Management = Using visual cues to make the status, performance, and flow of work immediately obvious.
Examples included in the question:
WIP board → Shows current work items and their status.
Kanban signals → Visual triggers (cards, lights, bins) that signal need for action.
Process maps → Visual depiction of process steps and flow.
Key takeaway:
All three are valid visual management tools because they convey information instantly without needing lengthy explanations.
Visual Management is about seeing the truth of the process at a glance.

## Slide 59
When a Measurement System Analysis (MSA) is designed, a common approach is to analyze 10
parts, 3 operators and 2 repetitions. An alternative design would be to analyze 5 parts, 3 operators
and 4 repetitions.
Why is it better to use more parts than more replicates?
When a part is measured four times as opposed to two times, there is an increased probability of remembering the measurement
There is no advantage except that using 5 parts is less costly than using 10 parts
Measuring twice only reduces the risk of changing the measured characteristic of the part
Using more parts provides a better estimate of the process variation
Notes: D
MSA Design Tip:
Parts → Capture process variation (the natural spread in actual product characteristics).
Replicates → Help estimate measurement error.
Why more parts > more replicates:
More parts = wider coverage of the process output range.
Gives a truer picture of actual variation in the system.
Improves the validity of Gage R&R analysis by ensuring you’re not just measuring the same limited range over and over.
Key takeaway: More variety in parts = better insight into how well your measurement system performs across the full spectrum of production.

## Slide 60
What is the most important starting point for a CTQ Flowdown?
a) Voice of the Business
b) Factors of Influence
c) Customer Complaints
d) Voice of the Customer
Notes: D
Why VOC is the starting point
CTQ (Critical to Quality) flowdown is all about translating customer needs into measurable, actionable requirements.
Voice of the Customer captures explicit and implicit expectations, preferences, and dislikes directly from the customer perspective.
Starting with VOC ensures the CTQs you define are aligned with customer value, not just internal goals.
How VOC drives the flowdown
Gather VOC → Surveys, interviews, focus groups, complaint logs, usage data.
Translate to needs → Identify customer priorities, pain points, and delight factors.
Define CTQs → Quantifiable specs that must be met to satisfy those needs.
Deploy through process → Flow these specs into design, production, and service activities.
Key takeaway: If you start anywhere other than VOC, you risk building a process that’s efficient for the business but irrelevant to the customer.

## Slide 61
How should the effectiveness of the implemented Root Cause Analysis (RCA) be validated?
Establishing proof by using the same indicator that demonstrated the problem originally
Confirming that the PCA (8D – D5) does solve the problem and does not introduce a new problem or defect
Obtaining the customers approval
Confirming that the Interim Containment Action will eliminate the problem
Notes: B
Why B can be considered correct
In the 8D problem‑solving process, D5 is the step for Permanent Corrective Action (PCA) — selecting and verifying the solution that addresses the root cause.
“Effectiveness” in this context isn’t just about seeing the symptom disappear once; it’s about confirming:
  The corrective action actually fixes the root cause, not just the symptom.
  It hasn’t caused unintended side effects — i.e., no new defects, safety risks, or performance issues elsewhere.
This verification often comes before full-scale implementation, so it’s a practical checkpoint step in the structured methodology.
How it differs from “same indicator” validation
Using the same indicator is a measurement technique for proving results.
B’s approach is more process‑centric — it checks the solution against the root cause logic and possible side effects, making sure the fix is robust.
In some training materials, B is emphasised as “the” validation step because it directly maps to the official 8D D5 deliverable.
Key takeaway
When following the 8D RCA framework, “effectiveness” validation is about confirming the PCA truly eliminates the root cause and does not introduce a new problem — this is the formal sign‑off that the solution works as intended.

## Slide 62
What is NOT the objective of a Standard Operating Procedure?
a) Detect the cause of a defect faster
b) List all required tools
c) Determination of process variation
d) Enable easy transfer of work activities
Notes: C
SOP Objective Exception: SOPs are not designed to determine process variation — they’re built to standardize work, list tools, and enable smooth transfer of activities.

## Slide 63
Given FMEA data:
Occurrence = remote (failure is unlikely), Severity = 7, Detection = 4.
What will most likely be the RPN?
a) 28
b) 56
c) 70
d) None of the above
Notes: A
RPN = 28 → Derived from Severity (7) × Occurrence (1) × Detection (4). Lowest possible occurrence score means the risk priority is significantly reduced

## Slide 64
An analysis of a Design of Experiments (DoE) shows an experimental error.
Which statement is true?
a) The experimental error is caused by interactions between 2 or more factors
b) The experimental error can be reduced only by improving the variability of the used materials
c) If the degrees of freedom increase, the experimental error will decrease
d) This experimental error is due to the inherent variability within the factor-level combinations
Notes: D
In a Design of Experiments (DoE), experimental error is the unexplained variation in the response variable after accounting for all known factor effects. This variation is inherent — coming from small, uncontrollable fluctuations in materials, measurement systems, environment, operator differences, etc.
It represents the noise present even when factor levels are fixed
Not due to: Factor interactions, degrees of freedom, or a single variability source alone.

## Slide 65
Compared to a two-level factorial experiment, which of the following is an advantage of an
experiment in three levels?
a) The experiment only works with attribute data
b) Non-linear behavior can be detected
c) The design is similar to an OFAT experiment
d) Interaction effects can be estimated
Notes: B
Two‑level factorial designs (e.g., high/low) capture linear effects of factors and their interactions, but they can’t detect curvature in the response.
Three‑level designs introduce a middle level (low, medium, high), which allows the model to:
Identify non‑linear (curvature) relationships between factor levels and the response.
Fit quadratic terms in the model.
This is especially useful when you suspect diminishing returns or optimum points that a straight line can’t reveal.
Why the others aren’t advantages here
a) Data type (attribute vs. variable) isn’t tied to the number of levels — you can run either with both.
c) OFAT (One‑Factor‑At‑a‑Time) is actually less efficient and not related to adding levels.
d) Interaction effects can already be estimated in two‑level designs — adding a third level isn’t required for that.

## Slide 66
Which activity might NOT reduce cycle time?
a) Practicing SMED
b) Utilising problem solving tools
c) Supervising people
d) Implementing 5S
Notes: C
Cycle time refers to the total time needed to complete a process from start to finish. Activities like SMED (Single‑Minute Exchange of Dies), problem‑solving tools, and 5S directly address efficiency, waste elimination, and process streamlining — all of which can shorten cycle time.
Supervision, while important for quality and compliance, is more about oversight and control rather than removing process waste or speeding up execution.

## Slide 67
In an FMEA, the Risk Priority Number is a product of 3 ratings: severity, occurrence and detection.
Please read the following statements about this:
1. The severity is rated from the customer's perspective
2. The occurrence is rated assuming there are no preventive measurements in place
3. The detection is rated taking into account the current detection controls
Which statements are true?
a) Statement 1 and 2 are true
b) Statement 1 and 3 are true
c) Statement 2 and 3 are true
d) All statements are true
Notes: B
1️⃣ Severity rated from the customer’s perspective ✅
True — Severity always reflects the potential impact on the end customer if the failure happens.
Ensures that the prioritisation of risks is based on customer harm or dissatisfaction, not internal inconvenience.
2️⃣ Occurrence rated assuming there are no preventive measures in place ❌ (in this interpretation)
Some organisations do consider existing preventive controls when scoring occurrence.
In that approach, occurrence reflects the actual observed frequency given the process as it operates today, not a “worst case with no prevention.”
That’s why this statement might be marked false in the context of your given answer.
3️⃣ Detection rated considering current detection controls ✅
True — Detection scoring is always based on the ability of the current detection methods to identify the failure before it reaches the customer.
The better the current detection methods, the lower the detection score.
In some FMEA methods, Severity = customer view, Detection = current controls. Occurrence is rated with existing prevention in mind, so Statement 2 is false — making Statements 1 & 3 true.

## Slide 68
Please read the following statements:
1. Most distributions have the same degrees of freedom
2. A chi-square test can be used for hypothesis testing
3. In all cases, the data is divided into bins / cells
When evaluating discrete data for goodness-of-fit to expected distributions, which statements are
true?
a) 1 and 2 only
b) 1 and 3 only
c) 2 and 3 only
d) 1, 2 and 3
Notes: C
1️⃣ Most distributions have the same degrees of freedom ❌
Degrees of freedom vary depending on the type of distribution and the number of estimated parameters.
For example, a chi‑square distribution’s degrees of freedom depend on the number of categories minus 1 (and adjustments for parameters estimated from the sample).
2️⃣ A chi‑square test can be used for hypothesis testing ✅
True — the Chi‑square goodness‑of‑fit test is a standard method for testing whether observed categorical data match an expected distribution.
3️⃣ In all cases, the data is divided into bins / cells ✅
True for goodness‑of‑fit testing — observed frequencies are compared to expected frequencies across bins or categories (cells).
This binning is fundamental to how the Chi‑square statistic is computed.
In goodness‑of‑fit tests for discrete data, Chi‑square is used for hypothesis testing and data is grouped into bins/cells. Degrees of freedom vary — so Statements 2 & 3 are true.

## Slide 69
Please see the table below:
What is the temp.*mat. interaction effect in this 2k factorial experiment?
a) -3
b) -1
c) 1
d) 2
Notes: C
Temp × Material Interaction Effect (2² Factorial)
Formula: Interaction Effect = [(Y₊₊ + Y₋₋) − (Y₊₋ + Y₋₊)] / 2
Using data: = [(70 + 62) − (74 + 56)] / 2 = (132 − 130) / 2 = 1

## Slide 70
What does a Kanban NOT trigger?
a) Production of product
b) Changeover of product
c) Transfer of product
d) Material handler to provide a workstation with raw materials
Notes: B
Kanban is a signal in pull systems (like Lean) that authorizes specific actions:
Production of product when downstream demand appears.
Transfer of product between stages.
Replenishment of raw materials to a workstation.
Changeover (switching production from one product type to another) is not triggered by Kanban itself — it’s typically part of scheduling or SMED (Single‑Minute Exchange of Dies) initiatives, not the Kanban signal.
Kanban does NOT trigger: Product changeover. Kanban does trigger: Start of production, transfer of items, and delivery of materials to point‑of‑use.

## Slide 71
The Belt wants to use a control chart to control a critical variable (Critical to Customer).
Which statement is correct?
a) The limits on the chart should reflect the variability of a stable process
b) Because the variable is critical to the customer, a response to any deterioration is necessary
c) The range between the control limits must be small to ensure on-time correction when the process shifts
d) Because the variable is critical for the customer, you must use the specification limits as control limits
Notes: A
Control Charts for Critical‑to‑Customer Variables
Control chart limits = statistical boundaries from a stable process.
Purpose: detect special‑cause variation, not meet specs.
Limits do not change because a variable is critical to the customer.
Control limits ≠ Specification limits — different sources & purposes.
Key point: Use process‑based control limits that reflect the variability of a stable process.

## Slide 72
Within SPC process control limits are based on:
a) Capability Studies
b) The product
c) The process specification
d) Customer requirements
Notes: A
In Statistical Process Control (SPC), control limits are calculated from process data — often collected during process capability studies when the process is stable and in control.
These limits represent natural variation (±3 σ from the process mean) and are not determined by:
The product itself
Written process specifications
Customer requirements
SPC Control Limits:
Derived from capability studies of a stable process.
Based on actual process performance, not external specs or requirements.
Purpose: detect special-cause variation early and maintain process stability.

## Slide 73
Which of the following statements about Statistical Process Control is true?
1. Customer specifications can be used as control limits on control charts
2. Control limits must reflect the process capability
3. You can't use control limits that are narrower than specification limits in the Control chart
a) Both 2 and 3 are true
b) Only 2 is true
c) Both 1 and 3 are true
d) All the statements are true
Notes: B
❌ Customer specs as control limits → Incorrect.
  Control limits are statistically calculated from process data during stable operation, not taken from customer specs.
✅ Control limits must reflect process capability → Correct.
  They should represent the actual natural variation of the process.
  Calculated as mean ± 3 σ from stable process data.
❌ Control limits can be narrower than spec limits → Possible and not forbidden.
  If the process variation is much smaller than the tolerance range, control limits will naturally be well inside specification limits.
SPC Truth:
Control limits = calculated from stable process data, reflecting process capability.
Do not use specification limits as control limits.
Control limits may be narrower than spec limits — this is often desirable for tighter process control.

## Slide 74
Which of the following is NOT a method for customer service data collection?
a) Customer visits
b) Complaint analyses
c) Customer surveys
d) Internal surveys
Notes: D
Customer service data collection focuses on direct customer-related inputs, such as:
Customer visits → Direct, face-to-face engagement to gather feedback.
Complaint analyses → Reviewing and categorizing issues raised by customers.
Customer surveys → Structured questionnaires to capture satisfaction, needs, and preferences.
Internal surveys → Gather feedback from employees or internal stakeholders, not customers, so they’re not considered a method for customer service data collection.
NOT a method of customer service data collection: Internal surveys. Customer service data is collected from direct customer interactions — e.g., visits, surveys, and complaint analysis.

## Slide 75
Calculate the Process Yield and Rolled Throughput Yield (RTY) for a process with four sequential process steps A to D
a) Process Yield = 62.5% and RTY = 56.3% b) Process Yield = 62.5% and RTY = 47.5% c) Process Yield = 47.5% and RTY = 62.5% d) Process Yield = 56.3% and RTY = 62.5%
Notes: B
Process Yield & Rolled Throughput Yield (RTY)
Process Yield = (Total Output ÷ Total Input) × 100
= (50 ÷ 80) × 100 = 62.5%
RTY = Step A Yield × Step B Yield × Step C Yield × Step D Yield
= (75/80) × (70/75) × (60/70) × (50/60) = 56.3%

## Slide 76
What are the four examples of wastes in a production process?
a) Overproduction, Waiting, Revenue and Movement
b) Waiting, Transport, Inventory and Movement
c) Work in Process (WIP), Overproduction, Transport and Inventory
d) Overproduction, Waiting, Movement, and insufficient inventory
Notes: B
In Lean Manufacturing and other process‑improvement methodologies, these are all considered examples of waste — activities that consume resources but do not add value to the customer:
Waiting → Idle time when work is delayed between steps.
Transport → Unnecessary movement of materials or products between processes.
Inventory → Excess raw materials, WIP, or finished goods beyond what’s needed.
Movement → Unnecessary motion by people or equipment that doesn’t add value.

## Slide 77
Which statistical distributions could be used to compare the means of two samples when the
standard deviations of the populations are unknown?
a) Normal distribution
b) F-distribution
c) Chi-square distribution
d) T distribution
Notes: D
When comparing means of two samples and the population standard deviations are unknown, the T distribution is used.
This is because:
  You estimate the standard error from sample data (introducing extra uncertainty).
  The T distribution adjusts for that uncertainty — it has heavier tails than the normal distribution, especially with small sample sizes.
As sample size increases, the T distribution approaches the normal distribution.
Use T distribution when comparing means of two samples if population σ is unknown. Based on sample standard deviation; accounts for extra variability. Becomes normal distribution as sample size grows.

## Slide 78
The outcome of a process is measured on a regular basis. What could be a measure for the
long-term process capability?
a) Levels A and B within which 80% of the occurrences fall
b) A process capability confidence interval with α = 0.05
c) A Ppk
d) A Cp
Notes: C
Long‑Term Process Capability
Ppk = Index for long‑term capability.
Reflects actual performance over time, including centering and overall variation.
Uses overall (long‑term) σ, not short‑term data.
More realistic than Cp/Cpk for ongoing capability assessment.
Key point: Ppk captures the true, sustained capability of a process.

## Slide 79
What is NOT an example of a VOC (Voice Of the Customer)?
a) A product that is delivered on time
b) A high turnover of the company that delivers the product
c) A good customer complaint process
d) A good product quality
Notes: B
VOC (Voice of the Customer) = Statements, requirements, or feedback directly expressing customer needs, expectations, and perceptions.
Examples of VOC include:
  Product delivered on time (a)
  Good complaint process (c)
  Good product quality (d)
High employee turnover (b) is an internal company metric — it affects operations indirectly but is not a direct expression of the customer’s voice.
NOT an example of VOC: High company turnover — it’s an internal performance measure, not customer‑expressed feedback.

## Slide 80
Given the following output of a gage R&R study:
A few statements are made about this:
1. The %contribution of Total Gage R&R is about 10%
2. There is no 'Part x Operator' interaction
3. The measurement system is classified as ideal
4. 'Part-to-Part' is the largest cause of Study variation
What can be deduced from the study?
a) 1, 2 & 3 only
b) 1, 2 & 4 only
c) 1, 3 & 4 only
d) 2, 3 & 4 only
Notes: B
Total Gage R&R (% Contribution) ≈ 9.52% → matches statement 1 ✔
Part × Operator interaction shows 0% or is absent → matches statement 2 ✔
Measurement system “ideal” usually means %GRR ≤ 1%. At ~9.5%, it’s acceptable but not ideal → statement 3 ✘
Part-to-Part variation dominates (% Study Variation ≈ 99.55%) → matches statement 4 ✔

## Slide 81
The manager of a clothing shop wants to improve the effectiveness of his employees. He plans to use a graphical tool to visualize the data. The manager records the number of customers that enter his shop per week and the number of customers that actually buy clothes per week.
In this situation, which graphical tool should this manager use?
a) A p-chart to plot the number of visitors and a np-chart to plot the proportion of buyers
b) A u-chart to plot the number of visitors and an np-chart to plot the proportion of buyers
c) A c-chart to plot the number of visitors and a p-chart to plot the proportion of buyers
d) A np-chart to plot the number of visitors and a p-chart to plot the proportion of buyers
Notes: C
1. Number of visitors per week
Data type: Attribute (count of occurrences).
What is being counted? – the number of customers entering (analogous to “number of defects” in quality control terms).
Area of opportunity: Constant (each week is one “unit of time” you’re counting over, so the basic opportunity definition doesn’t change).
According to the chart in the attachment, counts with a constant area of opportunity → C‑Chart.
2. Number of buyers per week (as a proportion of total visitors)
Data type: Attribute (buyers are the “successes” out of all visitors).
What is being measured? – proportion defective / proportion that meet a condition.
Sample size: Can vary (some weeks have more visitors than others).
From the selection flow, proportions with varying sample sizes → P‑Chart.
A c‑chart to plot the number of visitors and a p‑chart to plot the proportion of buyers

## Slide 82
Who should approve the Project Charter in a Lean Six Sigma Project?
a) The Black Belt
b) The Customer
c) The Champion
d) The board of the company
Notes: C
Why the Champion?
Role: A senior leader or manager who sponsors the project and has the authority to allocate resources and remove barriers.
Responsibility: Ensures the project is strategically aligned with business priorities and has organizational backing.
Authority: Can commit the organization to the goals laid out in the charter.
Other roles in context:
Black Belt: Leads the project day‑to‑day but doesn’t have the final authority to approve the charter.
Customer: Provides input on needs and requirements but doesn’t formally authorize internal projects.
Board of the company: Too high‑level for individual project charters; they set overall strategic direction.

## Slide 83
For what purpose is a SIPOC scheme used?
a) To identify the relation between the input and output variables of the process
b) To map the physical information flow within a company
c) To map the input, output and the major steps of a process
d) To minimize the risk of process control
Notes: C
A SIPOC diagram is a high‑level process mapping tool used in Lean Six Sigma (and other process improvement approaches) to get a clear, concise overview of a process before diving into the details.
SIPOC stands for:
Suppliers – who provides the inputs
Inputs – the resources, data, or materials used
Process – the major high‑level steps in the process
Outputs – what the process delivers
Customers – who receives the outputs
Purpose: It’s mainly used to map the inputs, outputs, and the major steps of a process so everyone involved has the same understanding of what’s being examined. It’s often done at the start of a project to define boundaries and scope.

## Slide 84
What does a Gage R&R quantify?
a) Both Reproducibility and Repeatability of a measurement system
b) Reproducibility of a measurement system
c) Repeatability of a measurement system
d) Reporting and Repeating of a measurement system
Notes: A
Gage R&R = Gage Repeatability and Reproducibility study.
Repeatability → Variation when the same operator measures the same part multiple times with the same equipment under the same conditions.
Reproducibility → Variation between different operators measuring the same part with the same equipment.
Together, these quantify measurement system variation — showing how much of the total observed variation comes from the gage (equipment + people) rather than the parts themselves.

## Slide 85
Which statement regarding a standard operating procedure (SOP) is true?
a) A SOP can never be replaced
b) A SOP can be replaced for a better one
c) A SOP is an advice
d) A SOP should describe a process in great detail
Notes: D
Standard Operating Procedure (SOP) = A documented, step-by-step set of instructions designed to ensure consistent, quality execution of a task or process.
An SOP must be clear, detailed, and unambiguous so that any competent person can follow it without confusion.
The aim is to maintain quality standards, comply with regulations, reduce variation, and ensure training consistency.
⚠ Why the other options don’t fit
a) ❌ SOPs can be replaced if outdated — change is part of continuous improvement.
b) ❌ Although true that SOPs can be updated, this statement misses the core definition of an SOP.
c) ❌ An SOP is not a casual “advice” — it’s a formal requirement.
💡 Pro tip: A well‑written SOP should answer who, what, when, where, why, and how — covering every necessary detail for perfect repeatability.

## Slide 86
Please read the following critical to quality (CTQ) steps:
1. Add additional CTQ levels as needed
2. Identify the customer's needs
3. Identify the customers
4. Validate the requirements with the customer
5. Identify the customer's basic requirements
What is the appropriate time sequence to arrange these CTQs from start to finish?
a) 2, 3, 5, 4, 1
b) 3, 2, 5, 1, 4
c) 3, 2, 4, 5, 1
d) 2, 3, 4, 1, 5
Notes: B
Identify the customers (3)
  You start by clarifying who the customer is — internal or external — because all further CTQ steps depend on knowing your audience.
Identify the customer's needs (2)
  Once the customer is defined, determine their explicit and implicit needs to guide requirement gathering.
Identify the customer's basic requirements (5)
  From the needs, extract the baseline measurable requirements — the essentials that define quality in their eyes.
Add additional CTQ levels as needed (1)
  Build in more detailed or higher‑level CTQs to capture critical subtleties or layered specifications.
Validate the requirements with the customer (4)
  Confirm with the customer that your interpreted requirements — basic and advanced — are correct, feasible, and complete.
🔍 Why option b makes sense
It follows the logical flow:
WHO ➡ WHAT THEY NEED ➡ BASE REQUIREMENTS ➡ EXPAND LEVELS ➡ VALIDATE
This ensures your CTQ tree is rooted in clear understanding before you start adding or confirming details.

## Slide 87
Process data used in the initial set-up of a process are assumed to have a normal distribution
with known σ. The nominal (target) is set at the center of the distribution, and the specification
limits are set at ± 3σ from the center.
What is the Cpk?
a) -0.25
b) 1.67
c) 1.00
d) 1.33
Notes: C
Cpk Calculation – Process Setup
Given: Process is centered at target, specs at ±3σ, σ is known, normal distribution.
USL = μ + 3σ, LSL = μ − 3σ.
Cpk formula: Cpk = min [ (USL − μ) ÷ (3 × σ), (μ − LSL) ÷ (3 × σ) ]
Substitution: Both sides = 1.0 → Cpk = 1.00.
Interpretation: Process variation fits exactly within spec limits (±3σ); capable but with zero margin for mean shift or increased variability.

## Slide 88
The Time Series Plot is usually one of the first charts a Belt would make.
What is the best reason to make this chart?
a) It tells something about potential causes
b) It tells us something about process capability
c) It tells us something about the stability of our process
d) It is a useful tool anyway
Notes: C
A Time Series Plot (or run chart) shows data points in chronological order, allowing you to see trends, cycles, shifts, or sudden changes.
One of the first things a Belt checks in any project is whether the process is stable over time — meaning only common cause variation is present and no special causes are influencing results.
Stability analysis is foundational: if a process isn’t stable, capability indices like Cp or Cpk aren’t meaningful, and deeper analysis could be misleading.
Why the other options miss the mark
a) Identifying potential causes requires further analysis (e.g., cause-and-effect diagrams, hypothesis tests).
b) Process capability requires a stable process first; capability comes later.
d) While true that it’s a useful tool, that’s too vague and not the best reason.
A Time Series Plot is primarily used early on to check process stability over time — the starting point for reliable analysis.

## Slide 89
In which time period and in what company was Lean developed?
a) Around 1940 at Honda
b) Around 1950 at Toyota
c) Around 1950 at Mitsubishi
d) Around 1965 at Subaru
Notes: B
Lean traces back to the Toyota Production System (TPS), developed in post‑WWII Japan — roughly around 1950.
Key figures: Taiichi Ohno, Shigeo Shingo, and Eiji Toyoda pioneered methods to maximize value, eliminate waste (muda), and continuously improve (kaizen).
TPS became the foundation for what is now called Lean Manufacturing worldwide.
Lean was born around 1950 at Toyota through the Toyota Production System, focusing on waste elimination, flow, and continuous improvement.

## Slide 90
The number of parts in a sample is called the:
a) Effect size
b) Number of distinct categories
c) Sample size
d) Degrees of freedom
Notes: C
Sample size (n) = the number of items, parts, or observations included in a particular sample.
It’s a fundamental parameter in statistics that impacts precision, confidence intervals, and the power of any analysis.
In manufacturing or quality control contexts, the sample size refers specifically to the count of parts inspected or measured from a lot or process run.
Why the other options don’t fit
a) Effect size → A measure of the magnitude of a difference or relationship, not a count.
b) Number of distinct categories → Relates to measurement system analysis (MSA), showing discrimination ability of the gage.
d) Degrees of freedom → The number of independent values that can vary in a calculation, not the total number of sampled items.
Sample size = the total number of parts or observations in your sample; a critical factor for accuracy and reliability of statistical conclusions.

## Slide 91
Variability in a sample or in a population can be described by different statistics.
Which statistic is the best and most common?
a) Mean
b) Range
c) Standard deviation
d) Interquartile range
Notes: C
Standard deviation (σ for population, s for sample) is the most widely used measure of variability because it accounts for all data points and shows the average distance of each value from the mean.
It’s more informative than:
  Range — which only uses min and max, ignoring all other values.
  Interquartile range (IQR) — focuses only on the middle 50% of data.
Standard deviation is also directly tied to many statistical methods, control charts, and capability indices (Cp, Cpk).
The standard deviation is the most common and effective statistic for describing variability, as it considers every value in the dataset and reflects overall spread.

## Slide 92
An X-bar & Range control chart is based on a sample size of 4. An employee mistakenly samples
6 parts instead of 4. He plots the average and the range of the 6 observations on the control chart.
Which statement is true?
a) The probability that the point in the Xbar chart shows an out of control condition is increased
b) The probability that the point in the R chart shows an out of control condition is increased
c) The points will always be plotted near the centre lines of the charts
d) Will not have any effect on the outcome of the control chart
Notes: B
R chart control limits are calculated based on the expected range for a specific subgroup size (n = 4 in this case).
If you accidentally take n = 6, the average range tends to be larger simply because with more observations per subgroup, the max–min spread naturally increases.
But the control limits on the R chart are still based on n = 4, so the plotted range for n = 6 is more likely to exceed the upper control limit (UCL) — falsely suggesting special‑cause variation.
Why not the others
a) The X‑bar chart’s control limits would actually shrink for a larger n (if recalculated), making points less likely to appear out‑of‑control — but here the limits aren’t adjusted, so its effect isn’t as pronounced as on the R chart.
c) Not true — data points could deviate depending on the mismatch in subgroup size and limits.
d) Incorrect — subgroup size matters; using the wrong n changes the variability patterns and the control chart interpretation.
Using a larger sample size than the chart was designed for inflates the plotted range, increasing the chance of false out‑of‑control signals on the R chart.

## Slide 93
Which levels of an organization participate in Kaizen?
a) CEO and top management
b) Production staff
c) Middle management
d) All, from CEO to cleaning staff
Notes: D
Kaizen = continuous improvement — a philosophy that everyone, regardless of role or rank, contributes to making processes better every day.
It thrives when improvement is a shared responsibility:
Top management → Sets vision, provides resources, and models commitment.
Middle management → Translates strategy into actionable team goals, facilitates improvements.
Frontline & support staff → Spot issues first‑hand, suggest practical fixes, and implement solutions.
Kaizen is most effective when all levels — from leadership to frontline — actively engage in small, ongoing improvements that build long‑term excellence.

## Slide 94
If the current operational availability of an automated assembly machine is not enough to meet
an increase in customer demand, what is the BEST way to improve the machine’s availability?
a) Maximize the speed of the machine
b) Increase the number of operators
c) Reduce breakdowns and delays
d) Hire specialist maintenance personnel
Notes: C
Operational availability reflects the proportion of time a machine is actually up and producing when it’s needed.
The biggest levers are minimising unplanned downtime and shortening recovery time — both directly tackled by preventing breakdowns and eliminating unnecessary delays.
This can include:
Implementing preventive and predictive maintenance
Improving spare parts readiness
Streamlining changeovers
Training operators for quick troubleshooting
Why not the others
a) Increasing speed won’t help if the machine is often stopped — you’re addressing the wrong constraint.
b) More operators don’t boost machine uptime unless downtime causes are operator‑related.
d) Specialist maintenance might help in some cases, but the broader and more sustainable approach is to attack root causes of downtime.
Boosting operational availability is best achieved by reducing breakdowns and delays, ensuring the machine is running when it’s needed most.

## Slide 95
In 5S, the application of line markings and labels belongs to?
a) Shine
b) Standardize
c) Sort
d) Straighten
Notes: D
Straighten (also known as Set in order) is the second step in the 5S methodology.
It focuses on organizing the workplace so every item has a clearly designated location — easy to find, easy to return.
Line markings help visually define storage areas, walkways, hazard zones.
Labels identify what goes where, making organization consistent and self‑explanatory.
📌 5S quick reference
Sort → Remove unnecessary items.
Straighten / Set in order → Organize & label everything for efficiency.
Shine → Clean and inspect regularly.
Standardize → Create consistent procedures.
Sustain → Maintain discipline and continuous improvement.
Applying line markings and labels is part of the Straighten step — ensuring tools, equipment, and materials are arranged visibly and logically for smooth workflow.

## Slide 96
Which tool can form part of "Visual Management"?
a) WIP board
b) Kanban signals
c) Process maps
d) All of the above
Notes: D
Visual Management uses simple, at‑a‑glance tools to make the state of a process visible so that anyone can quickly understand performance, issues, and next actions.
WIP board → Shows work‑in‑progress status, helping track flow and spot bottlenecks.
Kanban signals → Visual triggers (cards, lights, bins) that indicate when to start, stop, or replenish work.
Process maps → Diagram the workflow so everyone can see each step, handoff, and responsibility.
Since all three help make processes transparent and easier to manage visually, all are valid examples.
Visual Management tools range from WIP boards and Kanban signals to process maps — all aimed at making process status and needs visible, clear, and actionable at a glance.

## Slide 97
The locknuts manufactured by one supplier need to be compatible with bolts manufactured by
another supplier. The locknuts need to be produced within 0.02mm of the specified 6mm
diameter.
What tool should be used to measure products against this given tolerance?
a) Ruler
b) Sample mean
c) Standard deviation
d) Go/No go Gage
Notes: D
A Go/No Go Gage is designed to quickly check whether a part meets a specified tolerance — in this case, a 6 mm diameter within ± 0.02 mm.
Go end: Ensures the part is not too large (passes through the “go” gauge).
No‑go end: Ensures the part is not too small (doesn’t pass through the “no‑go” gauge).
This method is fast, reliable, and doesn’t require reading actual measurements, making it perfect for compatibility checks between components from different suppliers.
Why the others don’t fit
a) Ruler → Not precise enough for ± 0.02 mm tolerances.
b) Sample mean → A statistical measure, not a direct inspection tool.
c) Standard deviation → Describes variability, doesn’t determine pass/fail for a single item.
For tight dimensional tolerances like ± 0.02 mm, a Go/No Go Gage gives a quick, definitive pass/fail result — essential for ensuring part compatibility across suppliers.

## Slide 98
What are rework, over-production, inventory and motion examples of?
a) Noise
b) Value-Adding Activities
c) 5S Target Areas
d) Waste
Notes: D
In Lean methodology, rework, over‑production, excess inventory, and unnecessary motion are all classified as waste (muda in Japanese). They represent activities that consume resources — time, labor, materials, or space — without adding value from the customer’s perspective.
📌 The classic Seven Wastes include:
Overproduction – Making more than is needed or earlier than needed.
Waiting – Idle time between steps.
Transportation – Unnecessary movement of products or materials.
Overprocessing than necessary. – Doing more work
Inventory tying up capital – Excess stock.
Motion – Unnecessary movement of people or equipment.
Defects / Rework – Effort spent fixing errors.
Rework, over‑production, inventory, and motion are all forms of waste in Lean — targets for elimination to improve efficiency and deliver more value.

## Slide 99
One thousand units were examined to detect defects. Every unit has 5 opportunities for defects.
A total of 80 defects were found.
How many defects would be expected in one million opportunities?
a) 16000
b) 26666
c) 61458
d) 80000
Notes: A
DPMO = Defects ÷ Units × Opportunities per Unit ÷ 1 × 1,000,000
Step 1: 1,000 × 5 ÷ 5,000 × 80 ÷ 1 = 80 ÷ 5,000 × 1,000,000
Step 2: 80 ÷ 5,000 × 1,000,000
Step 3: 0.016 × 1,000,000
Step 4: 16,000

## Slide 100
What is the definition of Rolled Throughput Yield (RTY)?
a) Yield from the last step of a process that has a series of further steps to complete
b) Probability that a unit will pass every step within a process with zero defects
c) Number of defects from a single process step divided by the number of produced units
d) Total number of good units of all consecutive process steps divided by the number of produced units
Notes: B
Rolled Throughput Yield (RTY) measures the likelihood that a product or unit will successfully make it through all steps in a multi-step process without defects.
It accounts for the compounding effect of yields at each step — so even small defect rates at individual stages can significantly lower the overall RTY

## Slide 101
On a chicken farm, an automated egg inspector is used to sort out the eggs. The number of
rejected eggs per 10 trays of 30 eggs is recorded.
What is this type of data called?
a) Variable data
b) Attribute data
c) Categorical data
d) Discrete data
Notes: D
Attribute data refers to countable outcomes like pass/fail or defective/non-defective.
In this case, the how many eggs inspector is counting are rejected, not measuring physical properties.
This makes it attribute data, commonly used in quality control to track defects and calculate metrics like yield or DPMO.

## Slide 102
How many contrasts (main effects and interactions) does a 2-level full factorial with 4 factors
have?
a) 15
b) 16
c) 31
d) 32
Notes: A
In a 2-level full factorial design, the number of contrasts (main effects + interactions) is calculated as:
Total contrasts = 2^k - 1 ]
Where:
( k = ) number of factors
( 2^k = ) total number of treatment combinations
Subtract 1 to exclude the grand mean (overall average)
For 4 factors:
[ 2^4 - 1 = 16 - 1 = 15 \text{ contrasts} ]
These 15 contrasts include:
4 main effects (A, B, C, D)
6 two-way interactions (AB, AC, AD, BC, BD, CD)
4 three-way interactions (ABC, ABD, ACD, BCD)
1 four-way interaction (ABCD)

## Slide 103
Which of the following is NOT an effective analytical technique used to determine the root cause of
a problem submitted for corrective action?
a) Data analysis
b) Control charting
c) Operator observation
d) Pareto analysis
Notes: C
Control charting is primarily used for monitoring process stability over time, not for directly identifying the root cause of a problem. While it can signal that a problem exists (e.g., a process is out of control), it doesn't diagnose the cause.
Effective root cause analysis techniques include:
Data analysis – Examining patterns, trends, and metrics to uncover contributing factors
Operator observation – Watching how tasks are performed to identify errors or inefficiencies
Pareto analysis causes based on – Prioritizing frequency or impact (80/20 rule)
What control charts do:
Track variation over time
Detect shifts, trends, or out-of-control conditions
Help decide — but not how when to investigate to investigate

## Slide 104
What does a high OEE index indicate?
a) A machine does not need much maintenance
b) A machine is being exploited very effectively as compared to the so-called "ideal" machine
c) A machine is running optimally in terms of the 7 Lean 'waste' categories
d) A machine is running almost all the time with only a few stops
Notes: OEE measures how efficiently a machine is running compared to its ideal performance.
It combines Availability, Performance, and Quality into a single metric.
A high OEE means the machine has minimal downtime, runs at optimal speed, and produces few defects.
It reflects effective utilization of equipment, not just uptime or maintenance status.
OEE Formula: OEE = Availability × Performance × Quality

## Slide 105
Which of the following charts is used to monitor the number of defects per part?
a) NP Chart
b) U Chart
c) I-MR Chart
d) P Chart
Notes: B
A U Chart is a type of control chart used in statistical process control.
It monitors the average number of defects per unit (e.g., per part, item, or batch).
Useful when the sample size varies, and defects can occur multiple times per unit.
Ideal for tracking nonconformities in complex products or processes.
Key Formula: U = Total number of defects / Total number of units inspected

## Slide 106
Which communication technique has the widest universal acceptance?
a) The use of picture and charts
b) Translation to mathematical models
c) The use of translation tools
d) Standardization to English as the business language
Notes: A
Visual communication—through pictures, charts, and diagrams—is the most universally understood method.
It transcends language barriers, making complex ideas easier to grasp across cultures and literacy levels.
Widely used in engineering, business, education, and global collaboration.
Supports quick comprehension, especially in presentations, training, and technical documentation.
Examples:
Flowcharts, infographics, process diagrams, dashboards

## Slide 107
A Black Belt wants to know the process mean of a variable. Therefore, the Belt samples 10 units randomly from the process and calculates the sample average xbar=86 and standard deviation s=3.5. What is the 95% confidence interval for the population mean μ?
a) 83.50 < μ < 88.50 b) 79.14 < μ < 92.86 c) 85.31 < μ < 86.69 d) 84.37 < μ < 87.63
Notes: A
How to Use Minitab to Calculate This
Go to Stat > Basic Statistics > 1-Sample t
Choose Summarized data
Enter:
  Sample size = 10
  Mean = 86
  Standard deviation = 3.5
Click OK
View Results
  Minitab will display the 95% confidence interval in the output window.

## Slide 108
A project board does NOT:
a) Escalate problems during a project
b) Assign the necessary resources
c) Select the project leader
d) Select the problem
Notes: A
A project board is responsible for governance and oversight of a project. It typically:
Selects the project leader
Assigns resources
Escalates issues when needed
However, the problem or opportunity is usually identified before the board is formed—often by stakeholders, business analysts, or operational teams.
The board's role is to approve and support the project, not to define the problem itself.

## Slide 109
Let X be any random variable with mean μ and standard deviation σ. Now take a random sample
of size n.
What happens as n increases and the Central Limit Theorem is applied?
The distribution of sample average Xbar = (x1 + x2 + … + xn)/n approaches a normal distribution with mean μ and standard deviation σ/√n
The distribution of the sum Sn = x1 + x2 + …+ xn approaches a normal distribution with mean μ and standard deviation σ/√n
The distribution of X approaches a normal distribution with mean μ and standard deviation σ/√n
The distribution of the sum Sn = x1 + x2 + …+ xn approaches a normal distribution with mean n×μ and standard deviation σ/√n
Notes: A
The distribution of the sample average X̄ = (x₁ + x₂ + ... + xₙ) ÷ n approaches a normal distribution with:
- Mean = μ
- Standard deviation = σ ÷ √n
Key Points:
- CLT applies even if the original variable X is not normally distributed
- As n gets larger, the distribution of X̄ becomes approximately normal
- This allows us to use normal-based confidence intervals and hypothesis tests

## Slide 110
The term used to describe the risk of a Type I error in a hypothesis test is:
a) Alpha risk
b) Confidence level
c) Beta risk
d) Power
Notes: A
Type I error occurs when a true null hypothesis is wrongly rejected
The alpha risk (α) represents the probability of making this error
Common alpha levels: 0.05 (5%), 0.01 (1%)
It defines the threshold for statistical significance
Quick Definitions:
Alpha risk (Type I error): Rejecting a true null
Beta risk (Type II error): Failing to reject a false null
Confidence level: 1 − α
Power: 1 − β (probability of detecting a true effect)

## Slide 111
The following table shows the ages (X) and the systolic blood pressures (Y) of 12 people. Calculate the Pearson correlation coefficient r between X and Y.
a) Pearson correlation between Y and X = 0.892
b) Pearson correlation between Y and X = 0.932
c) Pearson correlation between Y and X = 0.768
d) Pearson correlation between Y and X = 0.853
X | 53 | 40 | 69 | 34 | 60 | 45 | 52 | 47 | 36 | 40 | 66 | 58
Y | 146 | 125 | 159 | 118 | 148 | 128 | 149 | 145 | 115 | 140 | 152 | 155
Notes: A
Steps in Minitab:
Enter the Data
  Open Minitab
  In Column C1, enter the Age values (X)
  In Column C2, enter the Blood Pressure values (Y)
Run the Correlation Analysis
  Go to Stat > Basic Statistics > Correlation
  Select both columns (C1 and C2)
  Click OK
Interpret the Output
  Minitab will display the Pearson correlation coefficient (r)
What r Tells You:
r > 0: Positive correlation (as age increases, blood pressure tends to increase)
r close to 1: Strong linear relationship
r close to 0: Weak or no linear relationship

## Slide 112
A study was conducted on the relationship between the weight of cars and their fuel consumption
in liters per 100 km. The calculated correlation coefficient was 0.39 with p-value 0.041. Later it was
discovered that the weighbridge showed too much measurement variation. This variation was
decreased and the weights of the same cars were re-measured.
What is the recalculated correlation coefficient?
a) Close to 0.39
b) Less than 0.39
c) Statistically insignificant
d) Higher than 0.39
Notes: D
The original correlation coefficient was 0.39, with a p-value of 0.041, indicating a statistically significant positive relationship.
However, the weight measurements had high variation, which likely introduced noise and weakened the observed correlation.
Once the measurement error was reduced, the true relationship between weight and fuel consumption became clearer.
This leads to a stronger correlation, so the recalculated coefficient would be higher than 0.39.
Key Concept:
Reducing measurement error improves data quality, which often results in stronger and more accurate correlations.

## Slide 113
As a Belt completes a LSS project he creates for the Process Owner a Control Plan.
Which portion of the Control Plan details the actions to be taken when the KPI’s indicate they may
be moving outside acceptable limits?
a) Operational procedures
b) Visual white board
c) Variance tracking
d) Out of Control Action Plan
Notes: D
The Out of Control Action Plan (OCAP) defines specific steps to take when KPIs deviate from acceptable limits. It includes:
  Immediate corrective actions
  Roles and responsibilities
  Escalation procedures
OCAP ensures process stability and helps sustain improvements after project completion.

## Slide 114
Poka Yoke is a quality technique. What is it used for?
a) Limit quality control to a final inspecton
b) Enable a 100% final inspection
c) Create a process with zero defects
d) Determine the number of quality inspectors
Notes: C
Poka Yoke means mistake-proofing and is used to prevent errors before they happen. It helps design processes that eliminate defects at the source, aiming for zero defects rather than relying on inspection.
Common examples include jigs, sensors, or design features that make incorrect operation impossible.

## Slide 115
Which principles does Just in Time (JIT) use?
a) Jidoka, Kanban and Cycle Time
b) Jidoka, Kaizen and Flow
c) Takt Time, Flow and Pull
d) Flow, Kanban and Kaizen
Notes: C
Just in Time (JIT) is a Lean strategy focused on producing only what is needed, when it's needed, and in the exact quantity required. It is built on three key principles:
Takt Time – Matches production rate to customer demand.
Flow – Ensures smooth and continuous movement of materials.
Pull – Triggers production based on actual demand, not forecasts.

## Slide 116
Calculate Takt Time based on the following data:
Customer demand: 80000 pcs per month
Working days: 21 days per month
Available: 2 shifts of 8 hours per day
Breaks: 1 hour per shift per day
a) 0.22 seconds per piece
b) 6.62 seconds per piece
c) 13.23 seconds per piece
d) 15.12 seconds per piece
Notes: C
Net time per shift: 8 hrs − 1 hr = 7 hrs
Total time per day: 2 shifts × 7 hrs = 14 hrs/day
Monthly available time: 14 hrs/day × 21 days = 294 hrs/month
Convert to seconds: 294 hrs × 3600 sec/hr = 1,058,400 sec/month
Takt Time: 1,058,400 sec ÷ 80,000 pcs = 13.23 sec/piece

## Slide 117
When performing an FMEA, what must a Belt do?
a) Identify the failure modes of the product and the causes of the failure
b) Calculate the expected number of failures in a given time interval
c) Estimate the probability that the customer will detect the failure
d) Estimate the probability of product success
Notes: A
FMEA (Failure Modes and Effects Analysis) is used to proactively identify potential failures in a product or process. A Belt must:
  Identify how the product or process could fail (failure modes).
  Determine why each failure might occur (causes).
This forms the foundation for evaluating risk and prioritizing corrective actions.

## Slide 118
What is NOT the purpose of the "Rolled Throughput Yield (RTY)" in the six sigma Define phase?
a) Spotting significant differences in yield
b) Providing a baseline metric
c) Using the calculation for customer analysis
d) Analysing a process flow for improvement ideas
Notes: C
RTY measures the cumulative yield of a multi-step process, showing how many units pass through all steps without defects. Its main purposes in the Define phase include:
  Spotting yield differences across steps
  Providing a baseline metric for improvement
  Analyzing process flow to identify weak points
RTY is not intended for customer analysis—it’s an internal performance metric, not a customer-facing tool.

## Slide 119
What does Value Stream Mapping (VSM) aim to achieve?
a) Visualization of patterns (trends, cycles etc.)
b) Generation of a large number of ideas in a short time
c) Reduction in activities that do NOT add value to a product
d) Prioritization of knowledge and opinions based on existing data
Notes: C
Value Stream Mapping (VSM) is a Lean tool used to visualize the entire flow of materials and information through a process. Its primary goal is to:
  Identify and eliminate non-value-adding activities
  Highlight waste such as delays, excess inventory, or unnecessary steps
  Streamline the process to improve efficiency and customer value
VSM focuses on value creation from the customer’s perspective.